## Slide 1
GERAS
Abdelmounaim DEBIECHE

## Slide 2: Ageing People
Well-being of ageing people: independent, active, happy, healthy, safe, …

## Slide 3: Societal Challenges of ageing people
Worldwide population is aging (by 2050 over 20% of the population will be aged 65 or over )
  - uneven demo-graphic composition
  - increase in age related illness
  - It places additional burdens on healthcare provision
  - the amount of informal support available will decrease due to a reduction in the ratio of working age people (15-64) to those older than 65.
Joseph Rafferty et al., 2013

## Slide 4: Demography of ageing people

## Slide 5: Ageing People
Living actively and independently at home
  Most older adults prefer to remain in the home of their choice as long as possible
  Older adults face challenges related to coping with daily life activities and making decisions when they live independently, especially when living alone.
Elisabete Pires, AAL 2015, Brussels

## Slide 6: Ageing People
ICT as an enabler for older adults to achieve their full capacities to stay active and live independently
  - estimated wealth of Europeans above 65 have
    3 billon € of revenues and wealth
  - it can also be considered as a socio-economic opportunity at large.
Elisabete Pires, AAL 2015, Brussels,
Rafael De Andrés Medina AAL 2015, Brussels

## Slide 7: Différent Solution for Ageing people

## Slide 8
Different Solutions for Ageing People

## Slide 9: Agenda
Internet Des Objets
Titre2
Titre3
Titre4
Notes: I will provide a broad overview of ThingML, present some challenges and interesting features that are missing in ThingML and suggest some potential contributions of our own.

## Slide 10: Internet Des Objets

## Slide 11: Internet Des Objets

## Slide 12: Object Abstraction
The first layer, the Objects (devices) or perception layer, represents the physical sensors of the IoT that aim to collect and process information. This layer includes sensors and actuators to perform different functionalities such as querying location, temperature, weight, motion, vibration, acceleration, humidity,

## Slide 13: Service Management
Service Management or Middleware (pairing) layer pairs a
service with its requester based on addresses and names. This layer enables the IoT application programmers to work with heterogeneous objects without consideration to a specific hardware platform. Also, this layer processes received data, makes decisions, and delivers the required services over the network wire protocols.

## Slide 14: Application Layer
The application layer provides the services requested by
customers. For instance, the application layer can provide temperature and air humidity measurements to the customer who asks for that data. The importance of this layer for the IoT is that it has the ability to provide high-quality smart services to
meet customers’ needs. The application layer covers numerous
vertical markets such as smart home, smart building, transportation,
industrial automation and smart healthcare [3], [17]–[19]

## Slide 15: Business Layer
The business (management) layer manages the overall IoT
system activities and services. The responsibilities of this layer are to build a business model, graphs, flowcharts, etc. based on the received data from the Application layer. It is also supposed to design, analyze, implement, evaluate, monitor, and develop IoT system related elements. The Business Layer makes it possible to support decision-making processes based on Big Data analysis. In addition, monitoring and management of the underlying four layers is achieved at this layer. Moreover, this layer compares the output of each layer with the expected output to enhance services and maintain users’ privacy [3], [18].

## Slide 16: Exemple

## Slide 17: Projet de GERAS
Objects
Service Management
Application Layer
Business Layer
Infrastructure Layer
Application Layer
Object Absetraction
GERAS

## Slide 18: Problématique
Comment manipuler les objets d’une manière simple et facile ?
Comment assurer les fonctionnalités de « Business layer» ?
Comment assurer la manipulation des différents objets hétérogènes dans une seule plate-forme ?

## Slide 19: Problématique 1
Comment manipuler les objets d’une manière simple et facile ?
Notes: Réponse :
* Développer un DSL.

## Slide 20: Proposition : Dsl
Proposition : un Dsl textuel / graphique

## Slide 21: Dsl: Type Declaration
enumeration Volume {V1; V2; V3;}
device Phone{
sensing receiveCall()
actuating ring(volume:Volume)
actuating setVolume(volume: Volume)
sensing pickedUp()
}
device LightBulb{
actuating on()
actuating off()
actuating blink()
}
device Timer{
actuating reset()
actuating set(delay : Volume)
sensing timeout()
}
device AlertDB{
actuating declareIncident(msg:string)
actuating alert()
}
device BodyDetector{
sensing detect()
actuating isPresent()
}
gateway Central

## Slide 22: Dsl: Network Configuration
configuration MyHome{
node gw : Central
node entranceBulb : LightBulb
node bathroomBulb : LightBulb
node kitchenBulb : LightBulb
node roomBulb : LightBulb
node ipPhone : Phone
node db : AlertDB
node bodydetector : BodyDetector
node timer : Timer
from entranceBulb to gw via IP
from bathroomBulb to gw via IP
from kitchenBulb to gw via IP
from roomBulb to gw via IP
from ipPhone to gw via IP
}

## Slide 23: Solution existante: ThingMl

## Slide 24: Problématique 2
Comment adapter les fonctionnalités de notre DSL selon le contexte ?

## Slide 25: Proposition

## Slide 26: Proposition: Business Rules
rule WaitBeforeBlink :
when (ipPhone.ring()) do {
timer.reset()} ; timer.set(10)
}
rule BlinkAndWait:
when (timer.timeout()) do {
LightBulb.blink()
||
(timer.reset() ; timer.set(120))
}
rule PickedUpQuick:
when (ipPhone.pickedUp()) do{
LightBulb.off()
}
rule NotPickedUpAfterBlinking:
when (timer.timeout()) do{
db.declareIncident(predefinedAlert)
||
bodydetector.detect()
||
timer.reset() ; timer.set(60)
}
rule Alert:
when (timer.timeout() and bodydetector.present()) do {
db.alert()
}

## Slide 27: Problématique 3
Comment assurer la manipulation des différents objets hétérogènes dans une seule plate-forme ?

## Slide 28: Problématique 3

## Slide 29: Conclusion

## Slide 30: Problématique
La croissance de la taux des personnes plus âgés peut
provoquer plusieurs problèmes :
Problème de mémoire
Problème de mouvement
Problème de prise de médicament.
Well-being of ageing people: independent, active, happy, healthy, safe, …

## Slide 31: Proposition
En utilisant la technologie moderne . Est-il possible de régler ce type de problème ?
Solution : IOT

## Slide 32: Internet des objets
Des généralités, des définitions.

## Slide 33: Exemple